Pine Wood Derby Track with IR Reflective Sensors
Chris and Jeff's Mad House
Accelerometer utilization in starting gate

---
It's for the kids right?

---
Challenges Addressed
- Physical/Mechanical design
  - Mounting IR Sensors
- Ground, Ground, Ground
  - Need common ground for all parts
  - Need solid connection to ground for things to work right
- Wires Everywhere – Where does this one go?
- Did you commit everything to the repo?
- Circuit Design
- Hard Fault – what does that mean? You can't reference Addr 0?

---
Most Serious Challenge
- There are nine external devices that generate interrupts. There are only 4 configurable external interrupts on the LPC1769; one of which has conflicts with the mode the board boots into.
- How to handle 9 external interrupts with only 3 modules?
- Use two four-channel MUX's to handle the IR sensors; one for each lane. That takes up EINT2 and EINT3. This solves two problems:
  - Shortage of EINT hardware for the project
  - Filters out spurious triggers from IR sensors
- Put the ADXL external interrupt on EINT1

---
It really is for the kids, right?

---
Hardware Components
- LPC1769 ARM Cortex M3 board
- LPC Xpresso Base Board
- MUX
- IR Sensors – TCND 5000 from Vishay Semiconductor
- ADXL345
- 7-segment LED Displays
- Lots of resistors, LEDs, OP Amps, and capacitors
- PC boards
- Power Supplies, Wall worts, wires, wires, ...

---
Firmware
- Display Task – displays a given decimal value to the correct display
- UART Task – Sends output over RS232 port to PC
- Reset Task – Handles button press and resets for another race.
- IR Sensor trigger interrupt handler
- ADXL345 interrupt handler
- Timer interrupt handlers
- UART interrupt handler
- Initialization and SPI code

---
It's for the CHILDREN!!!

---
Racing Flow
- Motion of gate triggers accelerometer interrupt starting timing logic
- As car passes over IR sensor
  - IR Sensor triggers interrupt
  - IR Sensor interrupt handler places struct with ID and time value into Display Task queue
  - IR Sensor interrupt handler places same struct on UART Task queue
- Display task receives struct from queue and displays time on display with ID corresponding to IR sensor ID

---
Task Priorities
- The Display and Reset tasks have priority 1
- The UART task has priority 2
  - Doesn't matter if it takes extra time for the UART to send data to the PC
  - Sending on the serial port is more resource intensive than displaying times and resetting
- This way UART gets whatever is left over and doesn't slow down the time critical functionality

---
External Interrupt Handlers
- IR Sensor external interrupt handlers (2)
  - One for each lane
  - Captured time for sensor and placed ID and time on Display task and UART task queues
  - Advance MUX to next IR sensor
- ADXL 345 external interrupt handler
  - Sets timer reference value

---
Questions?